JOB 97-95	ARCHIVES
		FINLAYSON LAKE AREA	-	SOUTHERN YUKON
			(Pathfinder, Cominco, Atna, YGC)
				March 11, 1998


This document describes the contents of the CD ROM in terms of:

	1)	the subdirectory structure of the CD ROM
	2)	the EM anomaly file structure and format
	3)	the line profile archive structure
	4)	the grid file structure and parameters.
	5)	the Geosoft plot files
	6)	the HPGL (Hewlett Packard) print files (not available)


1)	CD ROM Subdirectory Structure

The CD ROM has the following subdirectories:

	\doc		contains this document (README.DOC)
	\emanoms	contains the EM anomalies
	\profiles	contains the Geosoft .XYZ line profile archives
	\grids		contains the Geosoft .GRD files (grid files) and .ZON files
	\plots		contains the Geosoft .PLT files
	\HPGL		contains the HPGL (Hewlett Packard) 755cm print files
	

2)	EM Anomaly File Structure

ANOM.XYZ	-	ASCII data file of EM anomalies

The EM anomaly data file contains the following information:

1)	UTM Easting (metres)
2)	UTM Northing (metres)
3)	flight number
4)	line number
5)	time (hours)
6)	time (mins)
7)	time (secs)
8)	code (A, B, C, etc.)
9)	type for digitizing input (1, 2, 3, etc. - for Aerodat internal use only)
10)	bird height (metres)
11)	category (class based on conductance  0 through 6)
12)	inphase amplitude (ppm)
13)	quadrature amplitude (ppm)
14)	CTP (conductivity thickness product) (Seimens)
15)	depth (metres)

Example from ANOM.XYZ

     1        2        3      4    5  6  7    8   9   10    11     12       13      14   15
  370312.3 6796531.5  20    10010 19 48 31.2  A   1   28.    2    52.0    37.6     2.7    5.
  370424.5 6796693.0  20    10010 19 48 40.0  B   1   51.    2    31.3    24.6     2.1    0.
  370489.0 6796768.5  20    10010 19 48 43.8  C   1   52.    1    19.5    14.5     1.9    0.
  371659.8 6798140.5  20    10010 19 49 43.2  D   1   60.    0     3.2     4.4     0.3    6.
  372310.0 6798881.0  20    10010 19 50 12.8  E   1   35.    1    26.8    28.3     1.3    1.



3)	Line Profile Archive Structure

The profile archives contain the easting (X) coordinate and northing (Y) coordinates
which are standard UTMs in ground metres in the NAD27 (Clarke 1866) projection ellipsoid
using the standard UTM Zone #9 (central meridian of 129 degrees west longitude).  The local
DATUM shift used to convert from the WGS84 projection to NAD27 (Clarke 1866) was:

	DX	=	-10
	DY	=	158
	DZ	=	187


The profile archives are as follows:

PROF.XYZ	- MAG, altimeter, EM, resistivity and VLF profile archives

Also, in the profile subdirectory is a summary file PROF.XYZ.  This is a
summary of the .XYZ file and includes the line number, the number of data
points on the line and the minimum and maximum X, Y and time values for the line.



The following is a detailed description of the line profile archive which 
has been archived at a sample rate of 0.2 seconds (i.e. 5 readings per second):

XYZ 		FORMAT		UNITS			DESCRIPTION
COLUMN
   1		f10.1		metres			X = easting (NAD27, Zone 9)
   2		f10.1		metres			Y = northing (NAD27, Zone 9)
   3		f10.2		nanoteslas		final processed total field magnetics
   4		f10.1		metres			radar altimeter
   5		f10.1		metres			barometric altimeter
   6		f10.1		metres			digital elevation model
   7		f10.1		millivolts		power line monitor
   8		f10.1		ppm			861 Hz coplanar EM inphase
   9		f10.1		ppm			861 Hz coplanar EM quadrature
  10		f10.1		ppm			4765 Hz coplanar EM inphase
  11		f10.1		ppm			4765 Hz coplanar EM quadrature
  12		f10.1		ppm			33020 Hz coplanar EM inphase
  13		f10.1		ppm			33020 Hz coplanar EM quad.
  14		f10.1		ppm			912 Hz coaxial EM inphase
  15		f10.1		ppm			912 Hz coaxial EM quadrature
  16		f10.1		ppm			4365 Hz coaxial EM inphase
  17		f10.1		ppm			4365 Hz coaxial EM quadrature
  18		f10.4		log 10 ohm-metres	resistivity (from 861 coplanar EM)
  19		f10.4		log 10 ohm-metres	resistivity (from 4765 coplanar EM)
  20		f10.1		%			total field VLF
  21		f10.1		%			quadrature VLF
  22		f10.2		second after midnight	time
  23		f10.3		units			manual fiducials
  24		I6		units			flight number

Calculated Record Length     :         236

NOTE: The resistivity data in the profile archive is stored as LOG10.  Therefore, 
a reading of resistivity with a value of 1.2345 can be converted to ohm-metres by 
raising 10 to this power (i.e. 10 to the power of 1.2345).



4)	Grid File Structure and Parameters.

All grids have been written to CD ROM as standard Geosoft grids (.GRD).  The grids
have been archived as composite grids covering the entire area as well as two (2)
individual sheet grids.  The grid files and have the following characteristics:


COMPOSITE GRIDS

	X origin		338,500 metres east
	Y origin		6,796,000 north
	grid cell size		50 metres
	# columns (X)		686
	# rows (Y)		684


Sheet 1 Grids

	X origin		338,500 metres east
	Y origin		6,796,000 north
	grid cell size		50 metres
	# columns (X)		686
	# rows (Y)		301


Sheet 2 Grids

	X origin		338,500 metres east
	Y origin		6,810,600 north
	grid cell size		50 metres
	# columns (X)		686
	# rows (Y)		392



The following grids have archived:


FMAG.GRD		- composite total field magnetics (nT)
1FMAG.GRD		- sheet 1 total field magnetics (nT)
2FMAG.GRD		- sheet 2 total field magnetics (nT)

FCVG.GRD		- composite calculated vertical gradient magnetics (nT/M)
1FCVG.GRD		- sheet 1 calculated vertical gradient magnetics (nT/M)
2FCVG.GRD		- sheet 2 calculated vertical gradient magnetics (nT/M)

FRESL8P.GRD		- composite resistivity (from 861 coplanar EM)
1FRESL8P.GRD		- sheet 1 resistivity (from 861 coplanar EM)
2FRESL8P.GRD		- sheet 2 resistivity (from 861 coplanar EM)

FRESM4P.GRD		- composite resistivity (from 4765 coplanar EM)
1FRESM4P.GRD		- sheet 1 resistivity (from 4765 coplanar EM)
2FRESM4P.GRD		- sheet 2 resistivity (from 4765 coplanar EM)

FDTM.GRD                - composite digital elevation model (M)
1FDTM.GRD               - sheet 1 digital elevation model (M)
2FDTM.GRD               - sheet 2 digital elevation model (M)

FVLF.GRD		- composite total field VLF (%)
1FVLF.GRD		- sheet 1 total field VLF (%)
2FVLF.GRD		- sheet 2 total field VLF (%)

NOTE: The resistivity grids are in units of LOG10 ohm-M.

Also, the grids subdirectory contains the Geosoft colour palettes for each of
the above grids.  These have the same above prefix and a suffix of .ZON.




5)	the Geosoft plot files

The following Geosoft plot files (.ATT, .PLT) are the individual COMPONENT
plots used to assemble together to create the final black line plots and the
overlays combined with the colour grids to create the colour plots.


Dos File Name		WIN95 Filename	Description

ANOM1.ATT	.PLT	(anom1)		sheet 1 EM anomalies
ANOM2.ATT	.PLT	(anom2)		sheet 2 EM anomalies

BASEA1.ATT	.PLT	(BASEA1)	sheet 1 UTM/latlong marks
BASEA2.ATT	.PLT	(BASEA2)	sheet 2 UTM/latlong marks

TOPO1.ATT	.PLT	(topo1)		sheet 1 digitized topography (for colour plots)
TOPO2.ATT	.PLT	(topo2)		sheet 2 digitized topography (for colour plots)
				
FPATH1.ATT	.PLT	(fpath1)	sheet 1 flight path
FPATH2.ATT	.PLT	(fpath2)	sheet 2 flight path
				
BORDCVG1.ATT	.PLT	(bordcvg1)	sheet 1 gradient mag borders and surrounds
BORDCVG2.ATT	.PLT	(bordcvg2)	sheet 2 gradient mag borders and surrounds
				
CVG1.ATT	.PLT	(cvg1)		sheet 1 gradient mag contours
CVG2.ATT	.PLT	(cvg2)		sheet 1 gradient mag contours
				
BORDMAG1.ATT	.PLT	(bordmag1)	sheet 1 total field mag borders and surrounds
BORDMAG2.ATT	.PLT	(bordmag2)	sheet 2 total field mag borders and surrounds
				
MAG1.ATT	.PLT	(mag1)		sheet 1 total field mag contours
MAG2.ATT	.PLT	(mag2)		sheet 2 total field mag contours

BORDL8P1.ATT	.PLT	(bordl8p1)	sheet 1 low freq resist. borders and surrounds
BORDL8P2.ATT	.PLT	(bordl8p2)	sheet 2 low freq resist. borders and surrounds
				
RESL8P1.ATT	.PLT	(resl8p1)	sheet 1 low freq resist. contours
RESL8P2.ATT	.PLT	(resl8p2)	sheet 2 low freq resist. contours
				
BORDM4P1.ATT	.PLT	(bordm4p1)	sheet 1 mid freq resist. borders and surrounds
BORDM4P2.ATT	.PLT	(bordm4p2)	sheet 2 mid freq resist. borders and surrounds
				
RESM4P1.ATT	.PLT	(resm4p1)	sheet 1 mid freq resist. contours
RESM4P2.ATT	.PLT	(resm4p2)	sheet 2 mid freq resist. contours
				
BORDVLF1.ATT	.PLT	(bordvlf1)	sheet 1 VLF borders and surrounds
BORDVLF2.ATT	.PLT	(bordvlf2)	sheet 2 VLF borders and surrounds
				
VLF1.ATT	.PLT	(vlf1)		sheet 1 VLF contours
VLF2.ATT	.PLT	(vlf2)		sheet 2 vlf contours
				
BORDDTM1.ATT	.PLT	(borddtm1)	sheet 1 DTM borders and surrounds
BORDDTM2.ATT	.PLT	(borddtm2)	sheet 2 DTM borders and surrounds
				
DTM1.ATT	.PLT	(dtm1)		sheet 1 DTM contours
DTM2.ATT	.PLT	(dtm2)		sheet 2 DTM contours
				
BORDLEM1.ATT	.PLT	(bordlem1)	sheet 1 cp1/cx1 profile borders and surrounds
BORDLEM2.ATT	.PLT	(bordlem2)	sheet 2 cp1/cx1 profile borders and surrounds
				
L8CP1.ATT	.PLT	(l8cp1)		sheet 1 cp1 profiles
L8CP2.ATT	.PLT	(l8cp2)		sheet 2 cp1 profiles
L9CX1.ATT	.PLT	(l9cx1)		sheet 1 cx1 profiles
L9CX2.ATT	.PLT	(l9cx2)		sheet 2 cx1 profiles
				
BORDMEM1.ATT	.PLT	(bordmem1)	sheet1 cp2/cx2 profile borders and surrounds
BORDMEM2.ATT	.PLT	(bordmem2)	sheet2 cp2/cx2 profile borders and surrounds
				
M4CP1.ATT	.PLT	(m4cp1)		sheet 1 cp2 profiles
M4CP2.ATT	.PLT	(m4cp2)		sheet 2 cp2 profiles
M4CX1.ATT	.PLT	(m4cx1)		sheet 1 cx2 profiles
M4CX2.ATT	.PLT	(m4cx2)		sheet 2 cx2 profiles
				
BORDHEM1.ATT	.PLT	(bordhem1)	sheet 1 cp3 profile borders and surrounds
BORDHEM2.ATT	.PLT	(bordhem2)	sheet 2 cp3 profile borders and surrounds
				
H3CP1.ATT	.PLT	(h3cp1)		sheet 1 cp3 profiles
H3CP2.ATT	.PLT	(h3cp2)		sheet 2 cp3 profiles
				

The following Geosoft plot files (.ATT, .PLT) are composite plot files where
the individual components have been combined to create a complete overlay plot
file for merging with the colour grid to create the final colour contour plots.
For example, 1ACVGC.ATT/PLT is a composite of the following six (6) plot files:

	1)	ANOM1.ATT	.PLT	(anom1)		sheet 1 EM anomalies
	2)	BASEA1.ATT	.PLT	(BASEA1)	sheet 1 UTM/latlong marks
	3)	TOPO1.ATT	.PLT	(topo1)		sheet 1 digitized topography (for colour plots)
	4)	FPATH1.ATT	.PLT	(fpath1)	sheet 1 flight path
	5)	BORDCVG1.ATT	.PLT	(bordcvg1)	sheet 1 gradient mag borders and surrounds
	6)	CVG1.ATT	.PLT	(cvg1)		sheet 1 gradient mag contours



Dos File Name		WIN95 Filename	Description

1ACVGC.ATT	.PLT	(1acvgc)	final sheet 1 vert. grad. mag. colour overlay
2ACVGC.ATT	.PLT	(2acvgc)	final sheet 2 vert. grad. mag. colour overlay
				
1AMAGC.ATT	.PLT	(1amagc)	final sheet 1 total field mag colour overlay
2AMAGC.ATT	.PLT	(2amagc)	final sheet 2 total field mag colour overlay
				
1ARESL~1.ATT	.PLT	(1aresl8pc)	final sheet1 low freq. CP1 colour overlay
2ARESL~1.ATT	.PLT	(2aresl8pc)	final sheet2 low freq. CP1 colour overlay
				
1ARESM~1.ATT	.PLT	(1aresm4pc)	final sheet 1 mid freq. CP2 colour overlay
2ARESM~1.ATT	.PLT	(2aresm4pc)	final sheet 2 mid freq. CP2 colour overlay
				
1AVLFC.ATT	.PLT	(1avlfc)	final sheet 1 VLF colour overlay
2AVLFC.ATT	.PLT	(2avlfc)	final sheet 2 VLF colour overlay
				
1ADTMC.ATT	.PLT	(1adtmc)	final sheet 1 DTM colour overlay
2ADTMC.ATT	.PLT	(2adtmc)	final sheet 2 DTM colour overlay
				
1ALEM.ATT	.PLT	(1alem)		final sheet 1 low freq. EM profile plot
2ALEM.ATT	.PLT	(2alem)		final sheet 2 low freq. EM profile plot
				
1AMEM.ATT	.PLT	(1amem)		final sheet 1 mid freq. EM profile plot
2AMEM.ATT	.PLT	(2amem)		final sheet 2 mid freq. EM profile plot
				
1AHEM.ATT	.PLT	(1ahem)		final sheet 1 high freq. EM profile plot
2AHEM.ATT	.PLT	(2ahem)		final sheet 2 high freq. EM profile plot



6)	the HPGL (Hewlett Packard) print files

The final plotting was performed using an HP755cm colour plotter and all final
graphics print files were generated using this driver.  As such, these HPGL print
files included in this archive will only plot on an HP755cm (OR HIGHER level) version
plotter (HP supports ONLY upward compatability).  The files MAY plot on lower level
plotters such as HP750 or HP650 BUT this is not guaranteed.


THe following files are the final BLACK LINE HPGL print files:


Dos Filename	Bytes		WIN95 Filename	Description

1ABASE.PRN	1,022,847	1abase.prn	black line base map - sheet 1
2ABASE.PRN	1,013,505	2abase.prn	black line base map - sheet 2

1AINT.PRN	3,140,736	1aint.prn	black line interpretation underlay - sheet 1
2AINT.PRN	3,361,500	2aint.prn	black line interpretation underlay - sheet 2

1AMAG.PRN	3,712,787	1amag.prn	black line total field mag - sheet 1
2AMAG.PRN	3,983,715	2amag.prn	black line total field mag - sheet 2

1ACVG.PRN	3,747,309	1acvg.prn	black line vertical gradient mag - sheet 1
2ACVG.PRN	4,003,805	2acvg.prn	black line vertical gradient mag - sheet 2

1ARESL8P.PRN	3,507,356	1aresl8p.prn	black line low freq. resistivity - sheet 1
2ARESL8P.PRN	4,037,012	2aresl8p.prn	black line low freq. resistivity - sheet 2

1ARESM4P.PRN	3,520,392	1aresm4p.prn	black line mid freq. resistivity - sheet 1
2ARESM4P.PRN	4,042,812	2aresm4p.prn	black line mid freq. resistivity - sheet 2

1AVLF.PRN	3,505,790	1avlf.prn	black line VLF - sheet 1
2AVLF.PRN	3,732,564	2avlf.prn	black line VLF - sheet 2




The following are the final full COLOUR background (grid) print files:


Dos Filename	Bytes		WIN95 Filename	Description

1AMAGC.PRN	6,095,314	1amagc.prn	total field mag - sheet 1
2AMAGC.PRN	6,821,486	2amagc.prn	total field mag - sheet 2

1ACVGC.PRN	8,556,515	1acvgc.prn	vertical gradient mag - sheet 1
2ACVGC.PRN	10,170,958	2acvgc.prn	vertical gradient mag - sheet 2

1ALEM.PRN	4,380,565	1alem.prn	low freq. EM profies - sheet 1
2ALEM.PRN	4,050,093	2alem.prn	low freq. EM profies - sheet 2

1AMEM.PRN	4,384,084	1amem.prn	mid freq. EM profiles - sheet 1
2AMEM.PRN	4,070,924	2amem.prn	mid freq. EM profiles - sheet 2

1AHEM.PRN	3,897,203	1ahem.prn	high freq. EM profiles - sheet 1
2AHEM.PRN	3,448,611	2ahem.prn	high freq. EM profiles - sheet 2

1ARESL~1.PRN	6,483,920	1aresl8pc.prn	low freq. resistivity - sheet 1
2ARESL~1.PRN	6,497,643	2aresl8pc.prn	low freq. resistivity - sheet 2

1ARESM~1.PRN	6,530,818	1aresm4pc.prn	mid freq. resistivity - sheet 1
2ARESM~1.PRN	6,397,090	2aresm4pc.prn	mid freq. resistivity - sheet 2

1AVLFC.PRN	7,327,460	1avlfc.prn	VLF - sheet 1
2AVLFC.PRN	7,317,638	2avlfc.prn	VLF - sheet 2

1ASHADC.PRN	5,934,272	1ashadc.prn	shadow of total field mag - sheet 1
2ASHADC.PRN	5,789,041	2ashadc.prn	shadow of total field mag - sheet 2

1ADTMC.PRN	5,688,089	1adtmc.prn	digital elevation model - sheet 1
2ADTMC.PRN	5,484,409	2adtmc.prn	digital elevation model - sheet 2